## Slide 1
IEC 61131-9 · SDCI
IO‑Link
Smart last‑meter architecture for sensors, actuators, diagnostics, and fast replacement.
3-WIRE LINK
L+
24 V supply
L−
0 V return
C/Q
switching or IO-Link data
Power + bidirectional data on familiar industrial wiring.
Md Ratul Ahmed Alvi · Md Wasib Kamal Nirjon
Industrial Communication Standards· Electronic Engineering Hochschule Hamm-Lippstadt
Notes: Open by framing IO-Link as the smart last meter: not a fieldbus, but a digital point-to-point connection for the final sensor or actuator link. Mention that the seminar evaluates architecture, smart-device functions, and a packaging-cell use case.

## Slide 2
THE PROBLEM
Traditional sensor wiring hides useful information
TRADITIONAL 24 V WIRING
Only on/off or one analog value. No identity, no remote parameters, and no readable reason when a fault appears.
IO-LINK ENABLED
Process data, device identity, parameters, and diagnostic events travel on the same last-meter connection.
→
From a blind signal to a self-describing device.
Industrial Communication Standards · HSHL
02 / 12
Notes: The key contrast is not speed. The key contrast is information. A standard binary sensor can tell the PLC that something changed, but not what device it is, how it is configured, or why it failed. IO-Link adds a structured device channel while retaining familiar 24 V wiring.

## Slide 3
SCOPE
IO-Link is the digital interface for the last meter
FIELD DEVICE
Sensor / Actuator
point-to-point
▶
IO-LINK
Master
fieldbus · PROFINET
▶
CONTROL
PLC / HMI
✓
IT IS
IEC 61131-9, 3-wire 24 V — identity, parameters, status, and diagnostics.
✕
IT IS NOT
A multidrop fieldbus, a PROFINET replacement, or a channel for large camera data.
Industrial Communication Standards· HSHL
03 / 12
Notes: Stress the boundary: IO-Link sits between the device and the IO-Link master. The PLC still communicates through the plant fieldbus. IO-Link enriches the device side of that architecture.

## Slide 4
CONTEXT
Where IO-Link sits in an automation stack
1
CONTROL LEVEL
PLC + HMI
Decision logic and supervision.
2
GATEWAY LEVEL
IO-Link master
Bridge between IO-Link and the plant fieldbus.
3
FIELD LEVEL
Sensors + actuators
IO-Link devices live here.
One message: IO-Link belongs at the device edge.
04 / 12
Notes: Use this slide to prevent confusion with fieldbuses. The IO-Link master is the bridge: upstream it speaks a fieldbus, downstream it manages point-to-point device links.

## Slide 5
LAYER 1 · PHYSICAL
Physical connection and master-port classes
PIN ASSIGNMENT
L+
24 V supply
L−
0 V return
C/Q
switching or IO-Link data
C/Q BEHAVIOR
Starts as SIO switching, then changes to IO-Link after master negotiation.
M8 / M12 CONNECTORS
Unshielded cable up to 20 m for typical sensors.
PORT CLASS A / B
Class A serves standard sensors; Class B adds separately fused actuator power.
Industrial Communication Standards· HSHL
05 / 12
Notes: L+ and L- provide the 24 V supply. C/Q is the communication/switching line. SIO compatibility matters because an IO-Link device can behave like a standard switching sensor until IO-Link communication is established. Mention Class B when actuators need a separate power path.

## Slide 6
LAYER 2 · DATA
Fast process data, separate configuration
◆
Master initiates every exchange; devices respond.
CYCLIC
Process data up to 32 octets per direction per cycle, plus value status.
ACYCLIC
Parameters, identity, commands, warnings, and fault events run in parallel.
TRANSFER RATES
kbit/s
COM1
4.8
COM2
38.4
COM3
230.4
·Industrial Communication Standards HSHL
06 / 12
Notes: Cyclic data is the real-time process channel. Acyclic data is the engineering and diagnostic channel. Both are important: process values run continuously while parameter reads, writes, and event messages remain available.

## Slide 7
LAYER 3 · IODD
IODD makes device data usable
IODD
XML device description
A standard file that tells the master and tools how to read a device.
Readable engineering
Names, limits, and formats replace register guessing.
Remote parameter changes
Recipes and thresholds update without opening the cabinet.
Automatic restore
A replacement device receives the stored parameters.
Meaningful HMI events
16#5800 becomes “optical path contaminated.”
Industrial Communication Standards· HSHL
07 / 12
Notes: IODD is the translation layer for humans and engineering tools. It defines how the master and software interpret parameters, process data, limits, and event codes. The most practical benefit is faster commissioning and replacement.

## Slide 8
APPLICATION
Packaging cell: one master, four smart device links
Photoelectric
Bottle detect
Distance
Fill level
Pressure
Pneumatics
Valve
Sorting gate
IO-Link
▶
8
PORT
IO-Link master
PROFINET
▶
PLC + HMI
accept / reject logic
Industrial Communication Standards· HSHL
08 / 12
Notes: Use the packaging cell as a concrete mental model. Each field device gets its own IO-Link port. The master aggregates the device links and connects to the PLC/HMI over PROFINET. The value is not only process data, but also traceability, remote changeover, and readable diagnostics.

## Slide 9
METHOD
Requirements-based evaluation
Traceability
Type, serial, status
5/5
Changeover
Remote recipes
4/5
Diagnostics
Readable events
5/5
Replacement
Parameter restore
4/5
Port budget
One port per device
2/5
No measured latency claimed; timing is estimated from chain components.
09 / 12
Notes: Clarify the evaluation basis: standards and requirements, not lab measurements. This avoids overstating results. The timing slide is a chain estimate, not a benchmark. Port budget is intentionally scored lower because IO-Link uses one master port per device.

## Slide 10
PERFORMANCE
Timing depends on the whole automation chain
Delay
=
device cycle
+
master processing
+
fieldbus update
+
PLC scan
ESTIMATED ROUND TRIP
▏ 10 ms target
COM1 only
22
COM2 only
6
COM3 only
3
COM2 + slow PLC
14
TAKEAWAY
COM2/COM3 can meet the IO-Link portion. A slow PLC scan can still break the budget.
Illustrative chain estimate — milliseconds, not benchmarked.
10 / 12
Notes: Use the chart as an illustrative chain model. COM1 misses the 10 ms target. COM2 and COM3 meet it alone, but the PLC scan and fieldbus update must be included in the real budget. Do not present these as measured values from a test bench.

## Slide 11
DECISION GUIDE
Digital I/O, 4–20 mA, or IO-Link?
Digital I/O
DATA
On / off
DIAGNOSTICS
None
RECONFIGURATION
Fixed at install
BEST FOR
Lowest-cost limit switches
4–20 mA analog
DATA
One continuous value
DIAGNOSTICS
None
RECONFIGURATION
Fixed at install
BEST FOR
Simple analog over long cable runs
IO-Link
DATA
Process + parameters + events
DIAGNOSTICS
Readable event text
RECONFIGURATION
Remote in seconds
BEST FOR
Diagnostics and fast changeover
Industrial Communication Standards HSHL
11 / 12
Notes: This slide is the practical selection summary. Digital I/O is still fine when only a fixed on/off signal is needed. 4-20 mA remains useful for simple continuous values. Choose IO-Link when diagnostics, remote parameterization, traceability, or replacement speed matter more than the cheapest port.

## Slide 12
CONCLUSION
IO-Link is a smart last meter, not a fieldbus
1
Adds identity, parameters, and diagnostics to a familiar 3-wire 24 V link.
2
Use it when setup, diagnosis, or replacement downtime is the real cost.
3
Validate timing across device, master, fieldbus, and PLC scan.
4
Handle security at the system and network level.
Thank you. Questions?
Industrial Communication Standards · HSHL 12 / 12
Notes: Close by repeating the boundary: IO-Link does not replace the plant fieldbus. Its strength is making the final device link visible, diagnosable, and easier to maintain. Invite questions about the packaging-cell example, timing assumptions, or master-port planning.